## Slide 1
CEPDT PROJECT · SMART AGRICULTURE
Smart Irrigation System
From a Tinkercad Circuit Simulation to an Interactive 3D Digital Twin
Tinkercad · Arduino Uno
Three.js · WebGL Scene
Automated Moisture Control

## Slide 2
Project Overview
A two-part build: a working circuit prototype, and a real-time 3D visualization that brings it to life.
Sense Soil Moisture
A soil-moisture probe and TMP36 temperature sensor continuously feed live readings to the Arduino Uno.
Set a Custom Threshold
A 250 kΩ potentiometer lets the operator dial in exactly how dry the soil must get before watering starts.
Automate the Response
When soil crosses the threshold, the Arduino drives a DC pump motor, alert LEDs and a piezo buzzer automatically.
Display & Visualize
Readings appear on a 16×2 I2C LCD in the physical build — and on a live HUD inside a full 3D farm digital twin.

## Slide 3
System Architecture
The Arduino Uno sits at the center, reading sensors and driving outputs in real time.
INPUTS
Soil Moisture Sensor
Analog probe in the bed
TMP36 Sensor
Ambient temperature
Threshold Dial
250 kΩ potentiometer
Arduino Uno R3
the control loop
→
→
OUTPUTS
DC Pump Motor
Drives irrigation
16×2 I2C LCD
On-device readout
Buzzer + LEDs
Dry-soil alerts

## Slide 4
PART ONE
Circuit Design in Tinkercad
Prototyping the sensing and control hardware before writing a line of code.

## Slide 5
The Circuit
Simulated end-to-end in Tinkercad before any hardware was assembled.
Arduino Uno R3 — control unit
Soil Moisture Sensor — reads soil water content
TMP36 Sensor — ambient temperature
DC Pump Motor — irrigation actuator
16×2 I2C LCD — on-device readout
250 kΩ Potentiometer — threshold dial
Piezo Buzzer + LEDs — dry-soil alerts
Slide Switch + Resistors — power & current control
Full schematic — Tinkercad Circuits simulation
12
Components
1
Microcontroller
100%
Simulated First

## Slide 6
Bill of Materials
Every component used in the Tinkercad build.
Ref | Component | Qty
D1 | Red LED | 1
D2 | Green LED | 1
U1 | Arduino Uno R3 | 1
M1 | DC Motor | 1
SEN1 | Soil Moisture Sensor | 1
U2 | Temperature Sensor (TMP36) | 1
PIEZO1 | Piezo Buzzer | 1
— | Breadboard | 1
U7 | 16×2 I2C LCD (MCP23008, 0x20) | 1
Rpot3 | 250 kΩ Potentiometer | 1
S1 | Slide Switch | 1
R3, R4 | 1 kΩ Resistor | 2
R2 | 139 Ω Resistor | 1

## Slide 7
How the Circuit Works
From raw sensor signal to automatic watering, in four steps.
1
Sense
Soil-moisture and TMP36 sensors sample the bed and feed raw values to the Arduino every cycle.
2
Compare
The Arduino compares the live reading against the threshold set on the potentiometer dial.
3
Decide & Act
Below threshold: pump, red LED and buzzer switch on. Above it: the green LED stays lit and it idles.
4
Display
Moisture, temperature and system state are pushed to the 16×2 LCD in real time.

## Slide 8
PART TWO
A 3D Digital Twin, Built in Three.js
The same irrigation logic, reimagined as an explorable, real-time farm scene in the browser.

## Slide 9
Inside the Scene
A procedurally-textured farm — sky, soil, crops and machinery — rendered live with WebGL, zero external image assets.
Sky & Weather
Dynamic sky dome with drifting clouds and a toggleable rain system.
Water Tank & Crops
A modeled tank, windmill, shed and planted crop beds fill out the farmstead.
Control Pad Dial
A draggable in-scene dial sets the moisture threshold, mirroring the potentiometer.
Live HUD
Moisture, threshold, temperature, rain, tank and state, updated every frame.
Day / Night Cycle
Lighting, fog and sky tint shift smoothly between day and night.
Zero Image Assets
Grass, soil, concrete and wood textures are all generated on canvas at runtime.

## Slide 10
Play With It
The scene isn't just a render — it responds to input in real time.
Live HUD Readout
Moisture, threshold, temp, rain, tank and state at a glance.
Draggable Threshold Dial
Grab the control-pad dial to retune the watering threshold live.
One-Click Dry Soil
Trigger a dry-soil event instantly and watch the response cascade.
Rain Trigger
Simulate rainfall and watch the tank and HUD react.
Day / Night Toggle
Switch lighting and mood with a single click.
Orbit & Zoom
Drag to orbit the camera, scroll to zoom through the farm.

## Slide 11
Two Builds, One System
A physical prototype and a digital twin, both modeling the same irrigation logic.
Physical Prototype
TINKERCAD
Real Arduino Uno C++ logic on breadboard-accurate wiring
Validates sensor thresholds and component behavior before buying hardware
LCD, buzzer and LED feedback exactly as it runs on real hardware
Safe place to debug circuits, with zero risk of shorts
Digital Twin
THREE.JS / WEBGL
Full 3D farm environment rendered live in any modern browser
Real-time HUD plus interactive threshold dial, rain and day/night triggers
Zero build step — static HTML/JS/CSS loaded straight from a CDN import map
Ideal for demos, presentations and exploring “what if” scenarios instantly

## Slide 12
Impact & What's Next
What this project demonstrates — and where it can go.
IMPACT
FUTURE SCOPE
Bridges hardware prototyping and software visualization in one project
Demonstrates a full sense → decide → act embedded control loop
Built entirely from low-cost, widely available components
The digital twin makes the system explainable to a non-technical audience
Stream live sensor data from the real board into the 3D HUD
Solar-powered, field-deployable version of the circuit
Companion mobile app for remote threshold control
Multi-zone irrigation with per-bed moisture mapping

## Slide 13
Thank You
Smart Irrigation System — Tinkercad Circuit & Three.js Digital Twin
sohannarewadi12345@gmail.com